## Slide 1: Sequential Logic Design

## Slide 2: What will we learn?
How can a circuit remember a value
Different types of memorizing elements
Finite State Machines
How to write Finite State Machines in Verilog

## Slide 3: Introduction
Outputs of sequential logic depend on current and prior input values – it has memory.
Sequential Circuits:
  Give sequence to events which allows ordering of operations
  Need a special circuit to store the current state of circuit
Controlling when to change state
  ASYNCHROUNOUS As soon as circuit finishes, it moves to next state
  SYNCHRONOUS A global control signal (clock) that tells everyone when to move
(anarchic)
(communist) – THIS LECTURE

## Slide 4: Combinational + Memory = Sequential
Sequential Circuit
Combinational
Circuit
inputs
outputs
Memory
Element
We know Combinational Circuits, just need some MEMORY

## Slide 5: How can a circuit remember?
Bistable circuits can have two distinct states
  Once they are in one state, they will remain there.
The Loop keeps the state stable
0
1
0 = State 0

## Slide 6: How can a circuit remember?
Bistable circuits can have two distinct states
  Once they are in one state, they will remain there.
The Loop keeps the state stable
1
0
1 = State 1

## Slide 7: How can a circuit remember?
Bistable circuits can have two distinct states
  Once they are in one state, they will remain there.
But how can we move from one state to another?

## Slide 8: How can a circuit remember?
Bistable circuits can have two distinct states
  Once they are in one state, they will remain there.
But how can we move from one state to another?
  We add one switch to break the loop and at the same time add another switch that connects an input to the circuit

## Slide 9: The D Latch
D Latch is the basic bi-stable circuit used in modern CMOS.
  The clock controls the switches. Only one is active at a time.
  Traditionally the input is called D (Data) and the output Q

## Slide 10: The D Latch has two modes
Latch mode, loop is active, input disconnected, keeps state

## Slide 11: The D Latch has two modes
Latch mode, loop is active, input disconnected, keeps state
Transparent mode, loop is inactive, input is connected and propagates to output

## Slide 12: Summary D Latch
Simple bi-stable circuit
  Can be used to store a 0 or a 1.
Has two modes
  Transparent mode: input propagates to output
  Latch mode: the output is stored (also called opaque mode)
The clock controls the modes of operation.
  Depending on the type, it might be latch is transparent when Clk=1 or latch is transparent when Clk=0

## Slide 13: D Latch is commonly used... but…
It is a bit tricky to use
  There is a long transparent time, latch is not storing
  Problematic if we have a series of latches that form a pipeline
Usually used with alternating clocks for each stage
  If one latch is transparent at CLK=0 the next one is latching
  Make sure there are not two transparent latches in a row
A Flip-Flop (FF) is a circuit that combines two latches
  A Master latch that is transparent when CLK=0
  And a Slave latch that is transparent when CLK=1 (or vice versa)
Throughout this lecture we will use Flip-Flops

## Slide 14: Rising edge trigerred D Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge of CLK
  When CLK rises from 0 to 1, D passes through to Q
  Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered device because it is activated on the clock edge

## Slide 15: D Flip-Flop Internal Circuit
Two back-to-back latches (L1 and L2) controlled by complementary clocks
  When CLK = 0
    L1 is transparent
    L2 is opaque
    D passes through to N1
  When CLK = 1
    L2 is transparent
    L1 is opaque
    N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
D passes through to Q

## Slide 16: Registers
Multiple parallel flip-flops that store more than 1 bit

## Slide 17: Enabled Flip-Flops
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state

## Slide 18: Resettable Flip-Flops
Inputs: CLK, D, Reset
  The Reset is used to set the output to 0.
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 19: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop (see Exercise 3.10)
Synchronously resettable flip-flop?

## Slide 20: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop (see Exercise 3.10)
Synchronously resettable flip-flop?

## Slide 21: Settable Flip-Flops
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 22: Synchronous Sequential Logic Design
Breaks cyclic paths by inserting registers
  These registers contain the state of the system
  The state changes at the clock edge, so we say the system is synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock signal
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines

## Slide 23: Finite State Machine (FSM) consists of:
State register:
  Store the current state and
  Load the next state at the clock edge
  Sequential circuit
Next state logic
  Determines what the next state will be
  Combinational circuit
Output logic
  Generates the outputs
  Combinational Circuit

## Slide 24: Finite State Machine (FSM)
FSMs get their name because a circuit with k registers can be in one of a finite number (2k) of unique states.

## Slide 25: Finite State Machines (FSMs)
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state
  Mealy FSM: outputs depend on the current state and the inputs

## Slide 26: Finite State Machine Example
Traffic light controller
  2 inputs: Traffic sensors: TA, TB (TRUE when there’s traffic)
  2 outputs: Lights: LA, LB

## Slide 27: FSM Black Box
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB

## Slide 28: FSM State Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 29: FSM State Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 30: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 

## Slide 31: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0

## Slide 32: FSM Encoded State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X |  | 
0 | 0 | 1 | X |  | 
0 | 1 | X | X |  | 
1 | 0 | X | 0 |  | 
1 | 0 | X | 1 |  | 
1 | 1 | X | X |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 33: FSM Encoded State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 34: FSM Encoded State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S1’ = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S0’ = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 35: FSM Encoded State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S1’ = S1 xor S0 Simplification (Inspection or K-Maps)
S0’ = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 36: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 37: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow
Output | Encoding
green | 00
yellow | 01
red | 10

## Slide 38: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10

## Slide 39: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 40: FSM Schematic: State Register

## Slide 41: FSM Schematic: Next State Logic

## Slide 42: FSM Schematic: Output Logic

## Slide 43: FSM Timing Diagram

## Slide 44: FSM State Encoding
Binary encoding: i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit is HIGH at once
  I.e., for four states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler

## Slide 45: Moore vs. Mealy FSM
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last four digits it has crawled over are 1101. Design Moore and Mealy FSMs of the snail’s brain.

## Slide 46: State Transition Diagrams (snail - 1101)
Mealy FSM: arcs indicate input/output

## Slide 47: FSM Design Procedure
  Prepare
    Identify the inputs and outputs
    Sketch a state transition diagram
    Write a state transition table
    Select state encodings
  For a Moore machine:
    Rewrite the state transition table with the selected state encodings
    Write the output table
  For a Mealy machine:
    Rewrite the combined state transition and output table with the selected state encodings
  Write Boolean equations for the next state and output logic
  Sketch the circuit schematic

## Slide 48: Sequential Logic Design

## Slide 49: Last Week in Verilog
We have seen an overview of Verilog
Discussed behavioral and structural modeling
Showed combinational logic constructs
This week
Sequential circuit description in Verilog
Developing testbenches for simulation

## Slide 50: Combinational + Memory = Sequential
Sequential Circuit
Combinational
Circuit
inputs
outputs
Memory
Element
We know Combinational Circuits, just need some MEMORY

## Slide 51: Sequential Logic in Verilog
Define blocks that have memory
  Flip-Flops, Latches, Finite State Machines
Sequential Logic is triggered by a ‘CLOCK’ event
  Latches are sensitive to level of the signal
  Flip-flops are sensitive to the transitioning of clock
Combinational constructs are not sufficient
  We need new constructs:
    always
    initial

## Slide 52: always Statement, Defining Processes
always @ (sensitivity list)
statement;
Whenever the event in the sensitivity list occurs, the statement is executed

## Slide 53: Example: D Flip-Flop
module flop(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
q <= d; // pronounced “q gets d”
endmodule

## Slide 54: Example: D Flip-Flop
module flop(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
q <= d; // pronounced “q gets d”
endmodule
The posedge defines a rising edge (transition from 0 to 1).
This process will trigger only if the clk signal rises.
Once the clk signal rises: the value of d will be copied to q

## Slide 55: Example: D Flip-Flop
module flop(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
q <= d; // pronounced “q gets d”
endmodule
‘assign’ statement is not used within always block
The <= describes a ‘non-blocking’ assignment
  We will see the difference between ‘blocking assignment’ and ‘non-blocking’ assignment in a while

## Slide 56: Example: D Flip-Flop
module flop(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
q <= d; // pronounced “q gets d”
endmodule
Assigned variables need to be declared as reg
The name reg does not necessarily mean that the value is a register. (It could be, it does not have to be).
We will see examples later

## Slide 57: D Flip-Flop with Asynchronous Reset
module flop_ar (input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk, negedge reset)
begin
if (reset == ‘0’) q <= 0; // when reset
else q <= d; // when clk
end
endmodule
In this example: two events can trigger the process:
  A rising edge on clk
  A falling edge on reset

## Slide 58: D Flip-Flop with Asynchronous Reset
module flop_ar (input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk, negedge reset)
begin
if (reset == ‘0’) q <= 0; // when reset
else q <= d; // when clk
end
endmodule
For longer statements a begin end pair can be used
  In this example it was not necessary
The always block is highlighted

## Slide 59: D Flip-Flop with Asynchronous Reset
module flop_ar (input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk, negedge reset)
begin
if (reset == ‘0’) q <= 0; // when reset
else q <= d; // when clk
end
endmodule
First reset is checked, if reset is 0, q is set to 0.
  This is an ‘asynchronous’ reset as the reset does not care what happens with the clock
If there is no reset then normal assignment is made

## Slide 60: D Flip-Flop with Synchronous Reset
module flop_sr (input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
begin
if (reset == ‘0’) q <= 0; // when reset
else q <= d; // when clk
end
endmodule
The process is only sensitive to clock
  Reset only happens when the clock rises. This is a ‘synchronous’ reset
A small change, has a large impact on the outcome

## Slide 61: D Flip-Flop with Enable and Reset
module flop_ar (input clk,
input reset,
input en,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk, negedge reset)
begin
if (reset == ‘0’) q <= 0; // when reset
else if (en) q <= d; // when en AND clk
end
endmodule
A flip-flop with enable and reset
  Note that the en signal is not in the sensitivity list
Only when “clk is rising” AND “en is 1” data is stored

## Slide 62: Example: D Latch
module latch (input clk,
input [3:0] d,
output reg [3:0] q);
always @ (clk, d)
if (clk) q <= d; // latch is transparent when
// clock is 1
endmodule

## Slide 63: Summary: Sequential Statements so far
Sequential statements are within an ‘always’ block
The sequential block is triggered with a change in the sensitivity list
Signals assigned within an always must be declared as reg
We use <= for (non-blocking) assignments and do not use ‘assign’ within the always block.

## Slide 64: Summary: Basics of always Statements
module example (input clk,
input [3:0] d,
output reg [3:0] q);
wire [3:0] normal; // standard wire
reg [3:0] special; // assigned in always
always @ (posedge clk)
special <= d; // first FF array
assign normal = ~ special; // simple assignment
always @ (posedge clk)
q <= normal; // second FF array
endmodule
You can have many always blocks

## Slide 65: Summary: Basics of always Statements
module example (input clk,
input [3:0] d,
output reg [3:0] q);
wire [3:0] normal; // standard wire
reg [3:0] special; // assigned in always
always @ (posedge clk)
special <= d; // first FF array
assign normal = ~ special; // simple assignment
always @ (posedge clk)
q <= normal; // second FF array
endmodule
Assignments are different within always blocks

## Slide 66: Why does an always Statement Memorize?
module flop (input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
begin
q <= d; // when clk rises copy d to q
end
endmodule
This statement describes what happens to signal q
… but what happens when clock is not rising?

## Slide 67: Why does an always Statement Memorize?
module flop (input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
begin
q <= d; // when clk rises copy d to q
end
endmodule
This statement describes what happens to signal q
… but what happens when clock is not rising?
The value of q is preserved (memorized)

## Slide 68: Why does an always Statement Memorize?
module comb (input inv,
input [3:0] data,
output reg [3:0] result);
always @ (inv, data) // trigger with inv, data
if (inv) result <= ~data;// result is inverted data
else result <= data; // result is data
endmodule
This statement describes what happens to signal result
  When inv is 1, result is ~data
  What happens when inv is not 1 ?

## Slide 69: Why does an always Statement Memorize?
module comb (input inv,
input [3:0] data,
output reg [3:0] result);
always @ (inv, data) // trigger with inv, data
if (inv) result <= ~data;// result is inverted data
else result <= data; // result is data
endmodule
This statement describes what happens to signal result
  When inv is 1, result is ~data
  When inv is not 1, result is data
Circuit is combinational (no memory)
  The output (result) is defined for all possible inputs (inv data)

## Slide 70: always Blocks for Combinational Circuits
If the statements define the signals completely, nothing is memorized, block becomes combinational.
  Care must be taken, it is easy to make mistakes and unintentionally describe memorizing elements (latches).
Always blocks allow powerful statements
  if .. then .. else
  case
Use always blocks only if it makes your job easier

## Slide 71: Always Statement is not Always Practical…
reg [31:0] result;
wire [31:0] a, b, comb;
wire sel,
always @ (a, b, sel) // trigger with a, b, sel
if (sel) result <= a; // result is a
else result <= b; // result is b
assign comb = sel ? a : b;
endmodule
Both statements describe the same multiplexer
In this case, the always block is more work

## Slide 72: Sometimes Always Statements are Great
module sevensegment (input [3:0] data,
output reg [6:0] segments);
always @ ( * ) // * is short for all signals
case (data) // case statement
4'd0: segments = 7'b111_1110; // when data is 0
4'd1: segments = 7'b011_0000; // when data is 1
4'd2: segments = 7'b110_1101;
4'd3: segments = 7'b111_1001;
4'd4: segments = 7'b011_0011;
4'd5: segments = 7'b101_1011;
// etc etc
default: segments = 7'b000_0000; // required
endcase
endmodule

## Slide 73: The case Statement
Like if .. then .. else can only be used in always blocks
The result is combinational only if the output is defined for all cases
  Did we mention this before ?
Always use a default case to make sure you did not forget a case (which would infer a latch)
Use casez statement to be able to check for don’t cares
  See book page 202, example 4.28

## Slide 74: Non-blocking and Blocking Statements
always @ (a)
begin
a <= 2’b01;
b <= a;
// all assignments are made here
// b is not (yet) 2’b01
end
always @ (a)
begin
a = 2’b01;
// a is 2’b01
b = a;
// b is now 2’b01 as well
end
Non-blocking
Blocking
Values are assigned at the end of the block.
All assignments are made in parallel, process flow is not-blocked.
Value is assigned immediately.
Process waits until the first assignment is complete, it blocks progress.

## Slide 75: Why use (Non)-Blocking Statements
There are technical reasons why both are required
  It is out of the scope of this course to discuss these
Blocking statements allow sequential descriptions
  More like a programming language
If the sensitivity list is correct, blocks with non-blocking statements will always evaluate to the same result
  It may require some additional iterations

## Slide 76: Example: Blocking Statements
always @ ( * )
begin
p = a ^ b ; // p = 0
g = a & b ; // g = 0
s = p ^ cin ; // s = 0
cout = g | (p & cin) ; // cout = 0
end
Assume all inputs are initially ‘0’

## Slide 77: Example: Blocking Statements
always @ ( * )
begin
p = a ^ b ; // p = 1
g = a & b ; // g = 0
s = p ^ cin ; // s = 1
cout = g | (p & cin) ; // cout = 0
end
The process triggers
All values are updated in order
At the end, s = 1
Now a changes to ‘1’

## Slide 78: Same Example: Non-Blocking Statements
always @ ( * )
begin
p <= a ^ b ; // p = 0
g <= a & b ; // g = 0
s <= p ^ cin ; // s = 0
cout <= g | (p & cin) ; // cout = 0
end
Assume all inputs are initially ‘0’

## Slide 79: Same Example: Non-Blocking Statements
always @ ( * )
begin
p <= a ^ b ; // p = 1
g <= a & b ; // g = 0
s <= p ^ cin ; // s = 0
cout <= g | (p & cin) ; // cout = 0
end
The process triggers
All assignments are concurrent
When s is being assigned, p is still 0, result is still 0
Now a changes to ‘1’

## Slide 80: Same Example: Non-Blocking Statements
always @ ( * )
begin
p <= a ^ b ; // p = 1
g <= a & b ; // g = 0
s <= p ^ cin ; // s = 1
cout <= g | (p & cin) ; // cout = 0
end
Since there is a change in p, process triggers again
This time s is calculated with p=1
The result is correct after the second iteration
After the first iteration p has changed to ‘1’ as well

## Slide 81: Rules for Signal Assignment
Use always @(posedge clk) and non-blocking assignments (<=) to model synchronous sequential logic
  always @ (posedge clk)
  q <= d; // nonblocking
Use continuous assignments (assign …)to model simple combinational logic.
  assign y = a & b;

## Slide 82: Rules for Signal Assignment (cont)
Use always @ (*) and blocking assignments (=) to model more complicated combinational logic where the always statement is helpful.
Do not make assignments to the same signal in more than one always statement or continuous assignment statement

## Slide 83: Finite State Machines (FSMs)
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic

## Slide 84: Finite State Machine (FSM) consists of:
State register:
  Store the current state and
  Load the next state at the clock edge
  Sequential circuit
Next state logic
  Determines what the next state will be
  Combinational circuit
Output logic
  Generates the outputs
  Combinational Circuit

## Slide 85: FSM Example 1: Divide by 3
The output Y is HIGH for one clock cycle out of every 3. In other words, the output divides the frequency of the clock by 3.

## Slide 86: FSM in Verilog, Definitions
module divideby3FSM (input clk,
input reset,
output q);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
We define state and nextstate as 2-bit reg
The parameter descriptions are optional, it makes reading easier

## Slide 87: FSM in Verilog, State Register
// state register
always @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
This part defines the state register (memorizing process)
Sensitive to only clk, reset
In this example reset is active when ‘1’

## Slide 88: FSM in Verilog, Next State Calculation
// next state logic
always @ (*)
case (state)
S0: nextstate = S1;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
Based on the value of state we determine the value of nextstate
An always .. case statement is used for simplicity.

## Slide 89: FSM in Verilog, Output Assignments
// output logic
assign q = (state == S0);
In this example, output depends only on state
  Moore type FSM
We used a simple combinational assign

## Slide 90: FSM in Verilog, Whole Code
module divideby3FSM (input clk, input reset, output q);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
always @ (posedge clk, posedge reset) // state register
if (reset) state <= S0;
else state <= nextstate;
always @ (*) // next state logic
case (state)
S0: nextstate = S1;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
assign q = (state == S0); // output logic
endmodule

## Slide 91: FSM Example 2: Smiling Snail
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last four digits it has crawled over are 1101.
Moore
Mealy

## Slide 92: FSM Example 2: Verilog Definitions
module smilingsnail (input clk,
input reset,
input a,
output y);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
parameter S3 = 2’b11;
a/y

## Slide 93: FSM Example 2: State Register
// state register
always @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
This part defines the state register (memorizing process)
Sensitive to only clk, reset
In this example reset is active when ‘1’

## Slide 94: FSM Example 2: Next State Calculation
// next state logic
always @ (*)
case (state)
S0: if (a) nextstate = S1;
else nextstate = S0;
S1: if (a) nextstate = S2;
else nextstate = S0;
S2: if (a) nextstate = S2;
else nextstate = S3;
S3: if (a) nextstate = S1;
else nextstate = S0;
default: nextstate = S0;
endcase

## Slide 95: FSM Example 2: Output Assignments
// output logic
assign y = (a & state == S3);
In this example, output depends on state and input
  Mealy type FSM
We used a simple combinational assign

## Slide 96: FSM Example 2: Whole Code
module smilingsnail (input clk,
input reset,
input a,
output y);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
parameter S3 = 2’b11;
// state register
always @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always @ (*)
case (state)
S0: if (a) nextstate = S1;
else nextstate = S0;
S1: if (a) nextstate = S2;
else nextstate = S0;
S2: if (a) nextstate = S2;
else nextstate = S3;
S3: if (a) nextstate = S1;
else nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign y = (a & state == S3);
endmodule

## Slide 97: What Did We Learn?
Basics of Defining Sequential Circuits in Verilog
Always statement
  Is needed for defining memorizing elements (flip-flops, latches)
  Can also be used to define combinational circuits
Blocking vs Non-blocking statements
  = assigns the value immediately
  <= assigns the value at the end of the block
Writing FSMs
  Next state calculation
  Determining outputs
  State assignment

## Slide 98: What Did We Learn?
D Latch is the basic memorizing element
  Transparent mode, copies input to output
  Latch mode, keeps content
(Rising) Edge Triggered Flip-Flops are more practical
  Input is copied to output when the clock rises from 0 to 1
Finite State Machines
  Moore, output depends on only the current state
  Mealy, output depends on current state and the inputs.
Three Aspects of an FSM
  Holds the present state
  Calculate the next state
  Determine the outputs

## Slide 99: Tomorrow…
Timing in Combinational circuits
  Propagation and Contamination Delays
Timing for Sequential circuits
  Setup and Hold time
  How fast can my circuit work?
How timing is modeled in Verilog
Verification using Verilog
  How can we make sure the circuit works correctly
  Designing Testbenches