## Slide 1: Timing and Verification

## Slide 2: What will we learn
Timing in Combinational circuits
  Propagation and Contamination Delays
Timing for Sequential circuits
  Setup and Hold time
  How fast can my circuit work?
How timing is modeled in Verilog
Verification using Verilog
  How can we make sure the circuit works correctly
  Designing Testbenches

## Slide 3: The Goal Of Circuit Design Is To Optimize:
Area
  Net circuit area is proportional to the cost of the device
Speed / Throughput
  We want circuits that work faster, or do more
Power / Energy
  Mobile devices need to work with a limited power supply
  High performance devices dissipate more than 100W/cm2
Design Time
  Designers are expensive
  The competition will not wait for you

## Slide 4: Requirements Depend On Application

## Slide 5: Timing
Until now, we investigated mainly functionality
What determines how fast a circuit is and how can we make faster circuits?

## Slide 6: Propagation and Contamination Delay
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output

## Slide 7: Propagation & Contamination Delay
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation (not as fast as you think!)
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold

## Slide 8: Critical (Long) and Short Paths
Critical (Long) Path: tpd = 2 tpd_AND + tpd_OR
Short Path: tcd = tcd_AND

## Slide 9: Propagation times

## Slide 10: Propagation times

## Slide 11: Sequential Timing
Flip-flop samples D at clock edge
D must be stable when it is sampled
Similar to a photograph, D must be stable around the clock edge
If D is changing when it is sampled, metastability can occur
  Recall that a flip-flop copies the input D to the output Q on the rising edge of the clock. This process is called sampling D on the clock edge. If D is stable at either 0 or 1 when the clock rises, this behavior is clearly defined. But what happens if D is changing at the same time the clock rises?

## Slide 12: Input Timing Constraints
Setup time: tsetup = time before the clock edge that data must be stable (i.e. not changing)
Hold time: thold = time after the clock edge that data must be stable
Aperture time: ta = time around clock edge that data must be stable (ta = tsetup + thold)

## Slide 13: Output Timing Constraints
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)

## Slide 14: Dynamic Discipline
The input to a synchronous sequential circuit must be stable during the aperture (setup and hold) time around the clock edge.
Specifically, the input must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge

## Slide 15: Dynamic Discipline
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements

## Slide 16: Setup Time Constraint
The clock period or cycle time, Tc, is the time between rising edges of a repetitive clock signal. Its reciprocal, fc=1/Tc, is the clock frequency.
All else being the same, increasing the clock frequency increases the work that a digital system can accomplish per unit time.
Frequency is measured in units of Hertz (Hz), or cycles per second:
  1 megahertz (MHz) 106 Hz
  1 gigahertz (GHz) 109 Hz.

## Slide 17: Setup Time Constraint
The setup time constraint depends on the maximum delay from register R1 through the combinational logic.
The input to register R2 must be stable at least tsetup before the clock edge.
Tc >=

## Slide 18: Setup Time Constraint
The setup time constraint depends on the maximum delay from register R1 through the combinational logic.
The input to register R2 must be stable at least tsetup before the clock edge.
Tc >= tpcq + tpd + tsetup
tpd <=

## Slide 19: Setup Time Constraint
The setup time constraint depends on the maximum delay from register R1 through the combinational logic.
The input to register R2 must be stable at least tsetup before the clock edge.
Tc >= tpcq + tpd + tsetup
tpd <= Tc – (tpcq + tsetup)

## Slide 20: Hold Time Constraint
The hold time constraint depends on the minimum delay from register R1 through the combinational logic.
The input to register R2 must be stable for at least thold after the clock edge.
thold <

## Slide 21: Hold Time Constraint
The hold time constraint depends on the minimum delay from register R1 through the combinational logic.
The input to register R2 must be stable for at least thold after the clock edge.
thold < tccq + tcd
tcd >

## Slide 22: Hold Time Constraint
The hold time constraint depends on the minimum delay from register R1 through the combinational logic.
The input to register R2 must be stable for at least thold after the clock edge.
thold < tccq + tcd
tcd > thold - tccq

## Slide 23: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd =
tcd =
Setup time constraint:
Tc ≥
fc = 1/Tc =
Hold time constraint:
tccq + tcd > thold ?

## Slide 24: Timing Analysis
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps

## Slide 25: Fixing Hold Time Violation
tpd =
tcd =
Setup time constraint:
Tc ≥
fc =
Hold time constraint:
tccq + tcd > thold ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps

## Slide 26: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps

## Slide 27: Clock Skew
The clock doesn’t arrive at all registers at the same time
Skew is the difference between two clock edges
Examine the worst case to guarantee that the dynamic discipline is not violated for any register – many registers in a system!

## Slide 28: Preikestolen - Norway
600 m

## Slide 29: Stay away from both HOLD and SETUP !
<- HOLD
TIME
SETUP ->
TIME
SAFE

## Slide 30: How Do You Know That A Circuit Works?
You have written the Verilog code of a circuit
  Does it work correctly?
  Even if the syntax is correct, it might do what you want?
  What exactly it is that you want anyway?
Trial and error can be costly
  You need to ‘test’ your circuit in advance
In modern digital designs, functional verification is the most time consuming design stage.

## Slide 31: The Idea Behind A Testbench
Using a computer simulator to test your circuit
  You instantiate your design
  Supply the circuit with some inputs
  See what it does
  Does it return the “correct” outputs?

## Slide 32: Testbenches
HDL code written to test another HDL module, the device under test (dut), also called the unit under test (uut)
Not synthesizeable
Types of testbenches:
  Simple testbench
  Self-checking testbench
  Self-checking testbench with testvectors

## Slide 33: Example
Write Verilog code to implement the following function in hardware:
y = (b ∙ c) + (a ∙ b)
Name the module sillyfunction

## Slide 34: Example
module sillyfunction(input a, b, c,
output y);
assign y = ~b & ~c | a & ~b;
endmodule
Write Verilog code to implement the following function in hardware:
y = (b ∙ c) + (a ∙ b)
Name the module sillyfunction

## Slide 35: Simple Testbench
module testbench1(); // Testbench has no inputs, outputs
reg a, b, c; // Will be assigned in initial block
wire y;
// instantiate device under test
sillyfunction dut (.a(a), .b(b), .c(c), .y(y) );d
// apply inputs one at a time
initial begin // sequential block
a = 0; b = 0; c = 0; #10; // apply inputs, wait 10ns
c = 1; #10; // apply inputs, wait 10ns
b = 1; c = 0; #10; // etc .. etc..
c = 1; #10;
a = 1; b = 0; c = 0; #10;
end
endmodule

## Slide 36: Simple Testbench
Simple testbench instantiates the design under test
It applies a series of inputs
The outputs have to be observed and compared using a simulator program.
  This type of testbench does not help with the outputs
initial statement is similar to always, it just starts once at the beginning, and does not repeat.
The statements have to be blocking.

## Slide 37: Self-checking Testbench
module testbench2();
reg a, b, c;
wire y;
// instantiate device under test
sillyfunction dut(.a(a), .b(b), .c(c), .y(y));
// apply inputs one at a time
initial begin
a = 0; b = 0; c = 0; #10; // apply input, wait
if (y !== 1) $display("000 failed."); // check
c = 1; #10; // apply input, wait
if (y !== 0) $display("001 failed."); // check
b = 1; c = 0; #10; // etc.. etc..
if (y !== 0) $display("010 failed."); // check
end
endmodule

## Slide 38: Self-checking Testbench
Better than simple testbench
This testbench also includes a statement to check the current state
$display will write a message in the simulator
This is a lot of work
  Imagine a 32-bit processor executing a program (thousands of clock cycles)
You make the same amount of mistakes when writing testbenches as you do writing actual code

## Slide 39: Testbench with Testvectors
The more elaborate testbench
Write testvector file: inputs and expected outputs
  Usually can use a high-level model (golden model) to produce the ‘correct’ input output vectors
Testbench:
  Generate clock for assigning inputs, reading outputs
  Read testvectors file into array
  Assign inputs, get expected outputs from DUT
  Compare outputs to expected outputs and report errors

## Slide 40: Testbench with Testvectors
A testbench clock is used to synchronize I/O
  The same clock can be used for the DUT clock
Inputs are applied following a hold margin
Outputs are sampled before the next clock edge
  The example in book uses the falling clock edge to sample
Apply inputs
after some delay from the clock
Check outputs before the next clock edge
Clock period
HOLD MARGIN
SETUP MARGIN

## Slide 41: Testvectors File
We need to generate a testvector file (somehow)
File: example.tv – contains vectors of abc_yexpected
  000_1
  001_0
  010_0
  011_0
  100_1
  101_1
  110_0
  111_0

## Slide 42: Testbench: 1. Generate Clock
module testbench3();
reg clk, reset; // clock and reset are internal
reg a, b, c, yexpected; // values from testvectors
wire y; // output of circuit
reg [31:0] vectornum, errors; // bookkeeping variables
reg [3:0] testvectors[10000:0];// array of testvectors
// instantiate device under test
sillyfunction dut(.a(a), .b(b), .c(c), .y(y) );
// generate clock
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5; // 10ns period
end

## Slide 43: 2. Read Testvectors into Array
// at start of test, load vectors
// and pulse reset
initial // Will execute at the beginning once
begin
$readmemb("example.tv", testvectors); // Read vectors
vectornum = 0; errors = 0; // Initialize
reset = 1; #27; reset = 0; // Apply reset wait
end
// Note: $readmemh reads testvector files written in
// hexadecimal

## Slide 44: 3. Assign Inputs and Expected Outputs
// apply test vectors on rising edge of clk
always @(posedge clk)
begin
#1; {a, b, c, yexpected} = testvectors[vectornum];
end
Apply inputs with some delay (1ns) AFTER clock
This is important
  Inputs should not change at the same time with clock
Ideal circuits (HDL code) are immune, but real circuits (netlists) may suffer from hold violations.

## Slide 45: 4. Compare Outputs with Expected Outputs
// check results on falling edge of clk
always @(negedge clk)
if (~reset) // skip during reset
begin
if (y !== yexpected)
begin
$display("Error: inputs = %b", {a, b, c});
$display(" outputs = %b (%b exp)",y,yexpected);
errors = errors + 1;
end
// Note: to print in hexadecimal, use %h. For example,
// $display(“Error: inputs = %h”, {a, b, c});

## Slide 46: 4. Compare Outputs with Expected Outputs
// increment array index and read next testvector
vectornum = vectornum + 1;
if (testvectors[vectornum] === 4'bx)
begin
$display("%d tests completed with %d errors",
vectornum, errors);
$finish; // End simulation
end
end
endmodule
// Note: === and !== can compare values that are
// x or z.

## Slide 47: Golden Models
A golden model represents the ideal behavior of your circuit.
  Still it has to be developed
  It is difficult to get it right (bugs in the golden model!)
  Can be done in C, Perl, Python, Matlab or even in Verilog
The behavior of the circuit is compared against this golden model.
  Allows automated systems (very important)

## Slide 48: Why is Verification difficult?
How long would it take to test a 32-bit adder?
  In such an adder there are 64 inputs = 264 possible inputs
  That makes around 1.85 1019 possibilities
  If you test one input in 1ns, you can test 109 inputs per second
    or 8.64 x 1014 inputs per day
    or 3.15 x 1017 inputs per year
  we would still need 58.5 years to test all possibilities
Brute force testing is not feasible for all circuits, we need alternatives
  Formal verification methods
  Choosing ‘critical cases’
  Not an easy task