## Slide 1: Introduction to the FPGA and Labs
Notes: I am a doctoral student of Professor Capkun

## Slide 2: Lab Sessions
In HG E 26.1 and E 26.3
Tuesday 15:15-17:00 (also in HG E 19)
Wednesday 15:15-17:00
Friday 08:15-10:00
Friday 10:15-12:00
There is enough seating for you to hop around occasionally

## Slide 3: Labs in this Course
9 labs, 25 points in total
We will put the lab manuals online
Grading
  No need to hand in the reports! The questions are optional
  The assistants will check your work and note down your grade
  You should finish the labs within 1 week after they are announced
We want to help you successfully complete all the labs!
Notes: Feel free to let us know if you have issues
Assistant next year
Individual questions
Any questions?

## Slide 4: What will we learn?
What are programmable logic devices?
We will use a Field Programmable Gate Array (FPGA) in the exercises, what is this FPGA?
How does an FPGA work?
Information about the FPGA board we will use
Using Vivado to program the FPGA board
What will we do in the labs?
Notes: High-level last week
Basic building blocks
Learn with the FPGA programming

## Slide 5: Logic Arrays
Programmable logic arrays (PLAs)
  AND array followed by OR array
  Perform combinational logic only
  Fixed internal connections
Field programmable gate arrays (FPGAs)
  Array of configurable logic blocks (CLBs)
  Perform combinational and sequential logic
  Programmable internal connections
Notes: Combinational vs sequential
Example: counter

## Slide 6: Programming PLAs
Show how the PLA can be configured to realize:
  X = (A ∙ B ∙ C) + (A ∙ B ∙ C)
  Y = A ∙ B

## Slide 7: PLAs: Dot Notation

## Slide 8: FPGAs: Field Programmable Gate Arrays
Composed of:
  CLBs (Configurable Logic Blocks): perform logic
  IOBs (Input/Output Buffers): interface with outside world
  Programmable interconnection: connect CLBs and IOBs
Some FPGAs include other building blocks such as: multipliers and RAMs

## Slide 9: Typical FPGA Schematic

## Slide 10: CLBs: Configurable Logic Blocks
Composed of:
  LUTs (LookUp Tables): perform combinational logic
  Flip-flops (FF): perform sequential functions
  Multiplexers: connect LUTs and flip-flops
Notes: More details tomorrow and coming weeks

## Slide 11: CLB Configuration Example
Show how the CLB can be configured to realize:
  X = (A ∙ B ∙ C) + (A ∙ B ∙ C)
  Y = A ∙ B

## Slide 12: CLB Configuration Example
Show how the CLB can be configured to realize:
  X = (A ∙ B ∙ C) + (A ∙ B ∙ C)
  Y = A ∙ B

## Slide 13: FPGA Design Flow
A CAD tool (such as Vivado) is used to design and implement a digital system.
The user enters the design using schematic entry or an HDL.
Correct functionality is verified using simulation
A synthesis tool maps your description onto the FPGA.
The result is a bitfile that contains configures the CLBs and the connections between them and the IOBs.
The bitfile is downloaded to the FPGA

## Slide 14: The FPGA board for the Lab Exercises
Each lab group will use an FPGA board for the exercises.
Switches
LEDs
Seven-segment
displays
microUSB
(power/programming)
Power switch
Video out
FPGA chip
Buttons
USB

## Slide 15: What exactly is this FPGA board?
Contains a Programmable Logic Device (FPGA)
Various Interfaces
  Switches and Lights
  Video (VGA) Interface
  Keyboard/Mouse Interface
Support Circuits
  Circuits to store the configuration
  Power and Clock for all the components

## Slide 16: What will we do with the FPGA Board ?
At the end of the exercises, we will have built a 32-bit microprocessor running on the FPGA board.
  It will be a small processor, but it will be able to execute small programs.
Each week we will have a new exercise.
  Not all exercises will require the board.
You are encouraged to experiment with the board on your own.
  We may have some extra boards for those who are interested
  It is not possible to destroy the board by programming!

## Slide 17: Lab 1
Draw a comparator circuit on paper
Compare two inputs and output 1 if they are all the same
No FPGA programming, but you can try out the board

## Slide 18: Lab 2
Design a Full Adder and a 4-bit Adder
  Combinational circuit
Full Adder
  Takes 2 bits and output their sum and carry
4-bit Adder
  Instantiate 4 Full Adders to add 2 4-bit values
Use FPGA boards
  Input: switches
  Output: LEDs

## Slide 19: Lab 3
Show your results from Lab 2 on a seven segment display

## Slide 20: Lab 4
Implement a finite state machine using sequential circuit
Blinking LEDs for a car’s turn signals

## Slide 21: Lab 5
Towards implementing your very first processor
Implement your own Arithmetic and Logic Unit (ALU)
An ALU is an important part of the CPU
  Arithmetic operations: add, subtract, multiply, compare, …
  Logic operations: AND, OR, …

## Slide 22: Lab 6
Simulate your ALU design using a testbench
Validate that your ALU is functionally correct
Learn how to find and resolve problems in your circuit

## Slide 23: Lab 7
Assembly coding
  MIPS
Implement an program which you will later use to run on your processor
Calculate sum or number ranges
Image manipulation

## Slide 24: Lab 8
Learn how a processor is built
Complete your first design of a MIPS processor
Run a “snake”program

## Slide 25: Lab 9
Improve the performance of your MIPS processor by adding some new instructions
Multiplication
Bit shifting

## Slide 26: Vivado
Design circuits using Hardware Description Langauge (HDL)
Hardware Description Languages
  Verilog (this is the one we use in this course!)
  VHDL
FPGA Board
  Systhesis
  Implementation
  Program
Simulation
  Testbenches

## Slide 27: Typical design process on the FPGA board
Create a Vivado Project
Implement your circuit using Verilog code
Use the constraint file to specify which I/O to use
Implement your circuit
Generate the bitstream
Program to the board (target)

## Slide 28: A Short Tutorial
The AND gate
The output is true (1) only if both inputs are true (1).
Notes: Reading assignment: binary numbers

## Slide 29: Summary
Quick introduction of the FPGA
Short Tutorial on FPGA programming
  Getting started guide: https://reference.digilentinc.com/learn/programmable-logic/tutorials/basys-3-getting-started/start
  Demo: https://reference.digilentinc.com/reference/programmable-logic/basys-3/start
Overview of the labs
Tomorrow:
Combinational circuits