## Slide 1: Memories

## Slide 2: What will we learn today?
Common sequential building blocks
  Counters
  Shift registers
How can we store data?
Array organization of memories

## Slide 3: Common Sequential Building Blocks
Various Counters
  Up / down, program counters
Serial / Parallel Converters
  Serial In - Serial Out : Shift Register
  Serial In - Parallel Out
  Parallel In - Serial Out
  Parallel In - Parallel Out : Normal Register

## Slide 4: Counters
Increments on each clock edge.
  Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing

## Slide 5: Shift Register
Shift a new value in on each clock edge
Shift a value out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Symbol Implementation

## Slide 6: Shift Register with Parallel Load
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)

## Slide 7: Motivation: Memory Elements
Memories are large blocks
  A significant portion of a modern circuit is memory.
Memories are practical tools for system design
  Programmability, reconfigurability all require memory
Allows you to store data and work on stored data
  Not all algorithms are designed to process data as it comes, some require data to be stored.
  Data type determines required storage
    SMS: 160 bytes
    1 second normal audio: 64 kbytes
    1 HD picture: 7.32 Mbytes

## Slide 8: Die photograph of an Intel processor in 45nm

## Slide 9: Larger Memory Blocks

## Slide 10: How can we store data
Flip-Flops (or Latches)
  Very fast, parallel access
  Expensive (one bit costs 20+ transistors)

## Slide 11: How can we store data
Flip-Flops (or Latches)
  Very fast, parallel access
  Expensive (one bit costs 20+ transistors)
Static RAM (we will describe them in a moment)
  Relatively fast, only one data word at a time
  Less expensive (one bit costs 6 transistors)

## Slide 12: How can we store data
Flip-Flops (or Latches)
  Very fast, parallel access
  Expensive (one bit costs 20+ transistors)
Static RAM (we will describe them in a moment)
  Relatively fast, only one data word at a time
  Less expensive (one bit costs 6 transistors)
Dynamic RAM (we will describe them a bit later)
  Slower, reading destroys content (refresh), one data word at a time, needs special process
  Cheaper (one bit is only a transistor)

## Slide 13: How can we store data
Flip-Flops (or Latches)
  Very fast, parallel access
  Expensive (one bit costs 20+ transistors)
Static RAM (we will describe them in a moment)
  Relatively fast, only one data word at a time
  Less expensive (one bit costs 6 transistors)
Dynamic RAM (we will describe them a bit later)
  Slower, reading destroys content (refresh), one data word at a time, needs special process
  Cheaper (one bit is only a transistor)
Other storage technology (hard disk, flash)
  Much slower, access takes a long time, non-volatile
  Per bit cost is lower (no transistors directly involved)

## Slide 14: Array Organization of Memories
Efficiently store large amounts of data
  Consists of a memory array (stores data)
  Address selection logic (selects one row of the array)
  Readout circuitry (reads data out)
An M-bit value can be read or written at each unique N-bit address
  All values can be accessed, but only M-bits at a time
  Access restriction allows more compact organization

## Slide 15: Memory Arrays
Two-dimensional array of bit cells
  Each bit cell stores one bit
An array with N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M

## Slide 16: Memory Array: Example
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100

## Slide 17: Memory Arrays

## Slide 18: Types of Memories
Volatile memories (loses data when power is off)
  Static Random Access Memory (SRAM)
  Dynamic Random Access Memory (DRAM)
Non-volatile memories (keeps data even without power)
  Read Only Memory (ROM)
  Various forms of flash memory (i.e. EEPROM)

## Slide 19: Static Random Access Memory
Volatile: Stores data by cross coupled inverters, once data is stored the inverters keep the value (therefore static)
Historically called Random Access Memory, because data can be accessed in any order (unlike magnetic tapes which allowed only serial access)

## Slide 20: Dynamic Random Access Memory
Volatile: Stores data by charging a (small) capacitor
Problem is that the charge on the capacitor will slowly discharge (memory will forget the value) with time.
It is called Dynamic, because we have to refresh the contents before memory forgets what it stored.
The larger the capacitor, the longer it takes to forget
  This costs area, ingenious methods are used to increase capacitance

## Slide 21: Memory Array Organization
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output

## Slide 22: Memory Array Organization
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output
10
1
0
0
Active wordline

## Slide 23: How is Access Controlled ?
Access transistors configured as switches connect the bit storage to the bitline.
Access controlled by the wordline
DRAM
SRAM

## Slide 24: Read Only Memories
Non Volatile: Read Only Memories (ROM) can be made much denser
  No need to change the content (no storage transistors)
  Denser array
Used for keeping content that will not change
  Program of an embedded system
  Configuration data
  Look up tables
Re-writable (flash) memories are commonly used
  These are actually programmable, but writing is very slow
  From an application point of view identical to ROMs

## Slide 25: ROMs: Dot Notation

## Slide 26: ROM Storage

## Slide 27: ROM Logic
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0

## Slide 28: Logic with Memory Arrays
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B

## Slide 29: Logic with Memory Arrays
Called lookup tables (LUTs): look up output at each input combination (address)

## Slide 30: Multi-ported Memories
Port: address/data pair
3-ported memory:
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Small multi-ported memories are called register files

## Slide 31: Memory Arrays in Verilog
// 256 x 3 memory module with one read/write port
module dmem( input clk, // clock
input we, // write enable
input [7:0] a // 8-bit address
input [2:0] wd, // 3-bit write data
output [2:0] rd); // 3-bit read data
reg [2:0] RAM[255:0]; // Memory array, holds
// 256 entries each 3 bits wide
assign rd = RAM[a]; // Read access
always @(posedge clk) // with rising clock
if (we) // if write enable
RAM[a] <= wd; // write data is stored in array
endmodule

## Slide 32: What have we learned?
Different ways of storing data
  Registers
  Static Memory
  Dynamic Memory
Array organization
  Compact form
  One row active at a time