## Slide 1: Cache Architectures

## Slide 2: What Will We Learn ?
Brief review of how data can be stored
Memory System Performance Analysis
Caches

## Slide 3: Review: What were Memory Elements ?
Memories are large blocks
  A significant portion of a modern circuit is memory.
Memories are practical tools for system design
  Programmability, reconfigurability all require memory
Allows you to store data and work on stored data
  Not all algorithms are designed to process data as it comes, some require data to be stored.
  Data type determines required storage
    SMS: 160 bytes
    1 second normal audio: 64 kbytes
    1 HD picture: 7.32 Mbytes

## Slide 4: How Can We Store Data
  Flip-Flops (or Latches)
    Very fast, parallel access
    Expensive (one bit costs 20+ transistors)
  Static RAM
    Relatively fast, only one data word at a time
    Less expensive (one bit costs 6 transistors)
  Dynamic RAM
    Slower, reading destroys content (refresh), one data word at a time, needs special process
    Cheaper (one bit is only a transistor)
  Other storage technology (hard disk, flash)
    Much slower, access takes a long time, non-volatile
    Per bit cost is lower (no transistors directly involved)

## Slide 5: Array Organization of Memories
Efficiently store large amounts of data
  Consists of a memory array to store data
  The address selects one row of the array
  The data in the row is read out
An M-bit value can be read or written at each unique N-bit address
  All values in array can be accessed
  … but only M-bits at a time

## Slide 6: Memory Arrays

## Slide 7: Introduction
Computer performance depends on:
  Processor performance
  Memory system performance

## Slide 8: Introduction
Up until now, assumed memory could be accessed in 1 clock cycle
But that hasn’t been true since the 1980’s

## Slide 9: Memory System Challenge
Make memory system appear as fast as processor
Use a hierarchy of memories
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But we can only choose two!

## Slide 10: Memory Hierarchy

## Slide 11: Locality
Exploit locality to make memory accesses fast
Temporal Locality:
  Locality in time (e.g., if looked at a Web page recently, likely to look at it again soon)
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space (e.g., if read one page of book recently, likely to read nearby pages soon)
  If data used recently, likely to use nearby data soon
  How to exploit: when accessing data, bring nearby data into higher levels of memory hierarchy too

## Slide 12: Memory Performance
Hit: is found in that level of memory hierarchy
Miss: is not found (must go to next level)
  Hit Rate = # hits / # memory accesses = 1 – Miss Rate
  Miss Rate = # misses / # memory accesses = 1 – Hit Rate
Average memory access time (AMAT): average time it takes for processor to access data
  AMAT = tcache + MRcache[tMM + MRMM(tVM)]

## Slide 13: Memory Performance Example 1
  A program has 2,000 load and store instructions. 1,250 of these data values found in cache. The rest are supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Hit Rate =
Miss Rate =

## Slide 14: Memory Performance Example 1
  A program has 2,000 load and store instructions. 1,250 of these data values found in cache. The rest are supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Hit Rate = 1250/2000 = 0.625
Miss Rate = 750/2000 = 0.375 = 1 – Hit Rate

## Slide 15: Memory Performance Example 2
  Suppose a processor has 2 levels of hierarchy: cache and main memory:
  tcache = 1 cycle,
  tMM = 100 cycles
What is the AMAT of the program from Example 1?
AMAT =

## Slide 16: Memory Performance Example 2
  Suppose a processor has 2 levels of hierarchy: cache and main memory:
  tcache = 1 cycle,
  tMM = 100 cycles
What is the AMAT of the program from Example 1?
AMAT = tcache + MRcache(tMM)
= [1 + 0.375(100)] cycles
= 38.5 cycles

## Slide 17: Cache
A safe place to hide things
Highest level in memory hierarchy
Fast (typically ~ 1 cycle access time)
Ideally supplies most of the data to the processor
Usually holds most recently accessed data

## Slide 18: Cache Design Questions
What data is held in the cache?
How is data found?
What data is replaced?
We’ll focus on data loads, but stores follow same principles

## Slide 19: What data is held in the cache?
Ideally, cache anticipates data needed by processor and holds it in cache
But impossible to predict future
So, use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache. Next time it’s accessed, it’s available in cache.
  Spatial locality: copy neighboring data into cache too. Block size = number of bytes copied into cache at once.

## Slide 20: Cache Terminology
Capacity (C):
  the number of data bytes a cache stores
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 21: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by number of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks are in a single set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 22: Direct Mapped Cache

## Slide 23: Direct Mapped Cache Hardware

## Slide 24: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =

## Slide 25: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15 = 20%
Temporal Locality Compulsory Misses

## Slide 26: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =

## Slide 27: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10 = 100%
Conflict Misses

## Slide 28: N-Way Set Associative Cache

## Slide 29: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =

## Slide 30: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces conflict misses

## Slide 31: Fully Associative Cache
No conflict misses
Expensive to build

## Slide 32: Spatial Locality?
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = C/b = 8/4 = 2

## Slide 33: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =

## Slide 34: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks reduce compulsory misses through spatial locality

## Slide 35: Cache Organization Recap
Main Parameters
  Capacity: C
  Block size: b
  Number of blocks in cache: B = C/b
  Number of blocks in a set: N
  Number of Sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1

## Slide 36: Capacity Misses
Cache is too small to hold all data of interest at one time
  If the cache is full and program tries to access data X that is not in cache, cache must evict data Y to make room for X
  Capacity miss occurs if program then tries to access Y again
  X will be placed in a particular set based on its address
In a direct mapped cache, there is only one place to put X
In an associative cache, there are multiple ways where X could go in the set.
How to choose Y to minimize chance of needing it again?
  Least recently used (LRU) replacement: the least recently used block in a set is evicted when the cache is full.

## Slide 37: Types of Misses
Compulsory: first time data is accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy

## Slide 38: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)

## Slide 39: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)

## Slide 40: Caching Summary
What data is held in the cache?
  Recently used data (temporal locality)
  Nearby data (spatial locality, with larger block sizes)
How is data found?
  Set is determined by address of data
  Word within block also determined by address of data
  In associative caches, data could be in one of several ways
What data is replaced?
  Least-recently used way in the set

## Slide 41: Miss Rate Data
Bigger caches reduce capacity misses
Greater associativity reduces conflict misses
Adapted from Patterson & Hennessy, Computer Architecture: A Quantitative Approach

## Slide 42: Miss Rate Data
Bigger block size reduces compulsory misses
Bigger block size increases conflict misses

## Slide 43: Multilevel Caches
Larger caches have lower miss rates, longer access times
Expand the memory hierarchy to multiple levels of caches
  Level 1: small and fast (e.g. 16 KB, 1 cycle)
  Level 2: larger and slower (e.g. 256 KB, 2-6 cycles)
Even more levels are possible

## Slide 44: Intel Pentium III Die

## Slide 45: Virtual Memory
Gives the illusion of a bigger memory without the high cost of DRAM
Main memory (DRAM) acts as cache for the hard disk

## Slide 46: The Memory Hierarchy
Physical Memory: DRAM (Main Memory)
  Faster, Not so large, Expensive
Virtual Memory: Hard disk
  Slow, Large, Cheap

## Slide 47: The Hard Disk

## Slide 48: Virtual Memory
Each program uses virtual addresses
  Entire virtual address space stored on a hard disk.
  Subset of virtual address data in DRAM
  CPU translates virtual addresses into physical addresses
  Data not in DRAM is fetched from the hard disk
Each program has its own virtual to physical mapping
  Two programs can use the same virtual address for different data
  Programs don’t need to be aware that others are running
  One program (or virus) can’t corrupt the memory used by another
  This is called memory protection

## Slide 49: Cache/Virtual Memory Analogues
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number

## Slide 50: Virtual Memory Definitions
Page size: amount of memory transferred from hard disk to DRAM at once
Address translation: determining the physical address from the virtual address
Page table: lookup table used to translate virtual addresses to physical addresses

## Slide 51: Virtual and Physical Addresses
Most accesses hit in physical memory
But programs have the large capacity of virtual memory

## Slide 52: Address Translation

## Slide 53: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes

## Slide 54: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)

## Slide 55: Virtual Memory Example
What is the physical address of virtual address 0x247C?
  VPN = 0x2
  VPN 0x2 maps to PPN 0x7FFF
  The lower 12 bits (page offset) is the same for virtual and physical addresses (0x47C)
  Physical address = 0x7FFF47C

## Slide 56: How do we translate addresses?
Page table
  Has entry for each virtual page
  Each entry has:
    Valid bit: whether the virtual page is located in physical memory (if not, it must be fetched from the hard disk)
    Physical page number: where the page is located

## Slide 57: Page Table Example

## Slide 58: Page Table Example 1
What is the physical address of virtual address 0x5F20?

## Slide 59: Page Table Example 1
What is the physical address of virtual address 0x5F20?
  VPN = 5
  Entry 5 in page table indicates VPN 5 is in physical page 1
  Physical address is 0x1F20

## Slide 60: Page Table Example 2
What is the physical address of virtual address 0x73E0?

## Slide 61: Page Table Example 2
What is the physical address of virtual address 0x73E0?
  VPN = 7
  Entry 7 in page table is invalid, so the page is not in physical memory
  The virtual page must be swapped into physical memory from disk

## Slide 62: Page Table Challenges
Page table is large
  usually located in physical memory
Each load/store requires two main memory accesses:
  one for translation (page table read)
  one to access data (after translation)
Cuts memory performance in half
  Unless we get clever…

## Slide 63: Translation Lookaside Buffer (TLB)
Use a translation lookaside buffer (TLB)
  Small cache of most recent translations
  Reduces number of memory accesses required for most loads/stores from two to one

## Slide 64: Translation Lookaside Buffer (TLB)
Page table accesses have a lot of temporal locality
  Data accesses have temporal and spatial locality
  Large page size, so consecutive loads/stores likely to access same page
TLB
  Small: accessed in < 1 cycle
  Typically 16 - 512 entries
  Fully associative
  > 99 % hit rates typical
  Reduces # of memory accesses for most loads and stores from 2 to 1

## Slide 65: Example Two-Entry TLB

## Slide 66: Memory Protection
Multiple programs (processes) run at once
  Each process has its own page table
  Each process can use entire virtual address space without worrying about where other programs are
A process can only access physical pages mapped in its page table – can’t overwrite memory from another process

## Slide 67: Virtual Memory Summary
Virtual memory increases capacity
A subset of virtual pages are located in physical memory
A page table maps virtual pages to physical pages – this is called address translation
A TLB speeds up address translation
Using different page tables for different programs provides memory protection